## Slide 1
PHY 208
Prof. Aloke Kanjilal
Error analysis
(Spring Semester 2022)
Advanced Experimental Physics-I

## Slide 2: Motivation
Performing the experiment and collecting data is the beginning of the process of completing an experiment in science.
Error analysis is the study and evaluation of uncertainty in a measurement.
A result comprises of its value and some information on the “quality” of the result.
Note : Not all measurements have errors. If asked how many people there are in a room, one can give an exact number as an answer.
Precision – How reproducible
Accuracy – How close is it to the “true” value
“Error” (Uncertainty)

## Slide 3: Accuracy and Precision
High Precision
Low Accuracy
Low Precision
High Accuracy
High Precision
High Accuracy
True Value
Measurements

## Slide 4: Types of Errors
Systematic
Random
Due to built-in error in
the instrument either in
design or in calibration.
e.g. If the pointer in a stop watch is slightly bent so that it reads 1s instead of 0 seconds and you don’t notice this and start the clock and stop the clock at 10s mark, then you have taken the time period for only 9 s. This would be a systematic error in your result.
Repeated measurements
would not show a spread
in this error.
These lead to a spread or distribution of results on repetition of the particular measurement.
They may arise from fluctuations in either the physical parameters due to the statistical nature of the
particular phenomenon or the judgement of the experimenter,
e.g. variation in response
time or estimation in scale reading.

## Slide 5: Reducing uncertainty
Taking repeated measurements reduces the uncertainty of a measurement.
Mean value:
An experiment were repeated many, say N, times to get x1, x2, …, xk, …xN (N measurements of the same quantity, x)
The best estimate of the true value of x is then the
mean value of these measurements :
𝑥̅=(𝑥1+𝑥2+⋯+𝑥𝑘+⋯+𝑥𝑁)/N

## Slide 6: Measuring errors:
There are several different ways the distribution of the measured values of a repeated experiment such as discussed above can be specified.
Maximum Error : The maximum and minimum values of the data set, xmax and xmin, could be specified. In these terms, the quantity,
Δ𝑥𝑚ax=(𝑥𝑚ax−𝑥min)/2 is the maximum error.
Probable Error : Probable error, Δxprob, specifies the range 𝑥̅±Δ𝑥prob, which contains 50% of the measured values.
Average Deviation : The average deviation is the average of the absolute values of differences from the mean,
Δ𝑥AV=Σ|𝑥𝑘−𝑥̅|/𝑁
Standard Deviation :
We will use the standard deviation

## Slide 7: Reporting the measurement
Therefore any measurement is written down
as :
Where,
Standard deviation on mean
Standard Deviation

## Slide 8: Propagation of Errors
If a variable z=z(a1, a2, …, aN) depends on variables a1, a2, …, aN, which have independent errors (Δa1, Δa2, …, ΔaN), then the uncertainty in z is given by :
Few Examples :
Z = A + B Δ𝑍=√(Δ𝐴)2+(Δ𝐵)2
Z = A - B Δ𝑍=√(Δ𝐴)2+(Δ𝐵)2
Z = nA (n is an exact number) Δ𝑍=|𝑛|Δ𝐴

## Slide 9: Significant figures:
Non-zero digits or zeros between a number are significant.
549 – 3 sig. figs.
1.892 – 4 sig. figs.
4023 – 4 sig. figs.
For decimal’s zeros to the left of the first non-zero digit are not significant.
0.000034 – 2 sig. figs. Write
As 3.4 x 10-5
For decimal’s zeros to the right of a non-zero digit are significant.
2.00 – 2 sig. figs.
0.050 – 2 sig. figs. (5.0 x 10-2)

## Slide 10: Rules to express uncertainty
9.82 ± 0.02 9.82 ± 0.02385
10.0 ± 1.5 10.0 ± 2
4 ± 1 4 ± 0.5
The last significant figure in any result should be of the same order of magnitude (i.e. in the same decimal position) as the uncertainty.
The uncertainty should be rounded to one or two significant figures.

## Slide 11: Expressing uncertainty
A result is quoted as : A±∆A
This means that the “true value” lies between
a maximum value of A + ∆A and a
minimum value of A - ∆A
Also ,quote the relative error and percent error :
  Relative error = ∆A/A
  Percent error = (∆A/A)*100 %
Plotting errors on graphs :

## Slide 12: Graphing your results
If the slope or intercept of a line on a plot is the required calculated value (or the required value is calculated from these values) then the uncertainty of the slope and intercept will also be required.
First draw the best line possible, and then draw the two lines that just barely pass through the data.

## Slide 13
Fit to function
Final Result

## Slide 14: Log scale/Linear scale
Everyone is familiar with linear scales
Log (Logarithmic) scale is a scale of measurement that displays the physical quantity using intervals corresponding to orders of magnitude, rather than a standard linear scale.
Each unit increase on the logarithmic scale represents an exponential increase in the underlying quantity for the given base (10, in this case). So, we go as 1, 10, 10^2, 10^3 and so on..
Presentation of data on a logarithmic scale can be helpful when the data covers a large range of values.

## Slide 15: A semi-log graph

## Slide 16: A log-log graph

## Slide 17: Vernier Callipers
MSD = Main scale small division,
VSD = Vernier scale division
Least count = 1 MSD/(Number of VSD)
Note : Find out the least count of EVERY instrument before
Starting your readings.

## Slide 18: Reading the vernier caliper

## Slide 19: Screw Gauge
Least count = Pitch (Distance moved in one revolution/(Number of Divisions) =
0.5 mm/50 = 0.01 mm
Reading = Linear Scale reading + (coinciding circular scale x least count)
= 3.5 mm + (32 x 0.01)
= 3.5 + 0.32
= 3.82 mm